## Slide 1: SmartTraffic
Adaptive signal control built for lane-less Indian traffic
SIH PS90 · 15 controllers · 119 tests · every claim reproducible
Notes: One line: we built an adaptive traffic signal controller, and the part that is genuinely new is that it is designed for traffic without lane discipline. Everything I show you can be re-run from the repository with one command.

## Slide 2: Chennai loses 132 hours per commuter, per year
31:15
to travel 10 km
TomTom Traffic Index 2025
100.9%
evening congestion
a trip takes twice free-flow
16 km/h
peak speed
slower than a bicycle downhill
Signals are the cheapest lever a city has
New roads take years and land nobody has. Retiming the signals on a corridor is software. The catch is that the control theory every adaptive system is built on was written for traffic that queues in lanes — and Indian traffic does not.
Notes: Set up why signals matter, and plant the assumption that the whole deck turns on.

## Slide 3: What is standard, and what is ours
Established work — implemented, not claimed
Max-pressure control
Green-wave coordination
Emergency vehicle preemption
Transit signal priority
Reinforcement learning for signals
YOLO vehicle counting
Ours
A discharge model for lane-less mixed traffic, built from physical width and headway
Signal pressure measured in people per second of green, not vehicles or PCU
Two widely used evaluation metrics shown to be gameable — with the demonstration
Notes: Say this out loud early. Judges respect a team that knows which parts of its own project are textbook. It buys credibility for the part that is not.

## Slide 4: Signal theory assumes lane discipline
Two-wheelers filter into lateral gaps and cross two or three abreast where one car fits. What limits the stop line is lateral space — not a factor calibrated for moving traffic.
Notes: The pivot of the whole deck. Pause here.

## Slide 5: The conventional factor is 56% too high
Chart: Car-equivalents per vehicle
| Two-wheeler | Auto | Car | Bus
Static PCU (used today) | 0.5 | 0.8 | 1 | 3
Implied by real discharge | 0.32 | 0.66 | 1 | 1.8
56%
too high for a two-wheeler
Static PCU measures space in moving traffic. A junction asks a different question: how long does this queue take to clear?
Our model reproduces the textbook figure for cars exactly — 1800 veh/h/lane — so it departs from convention only where lane discipline does.
Notes: The car column being identical is the important detail. It shows we have not just invented numbers that suit us — where the old assumption holds, we agree with it exactly.

## Slide 6: That error becomes wasted green
Chart: Two-wheeler share of the queue
| 0% | 15% | 30% | 45% | 60% | 75%
Green allocated beyond need | 6 | 9.3 | 14.5 | 21.5 | 29.1 | 39.5
Indian urban arterials run at about 45%
At that mix a conventional controller holds the approach green 21.5% longer than the traffic needs. Those seconds are taken from the cross street while the road it was given to stands empty.
Robust to our own assumptions
Swept across the full plausible range of widths and headways, the error stays between +4.6% and +34.7%. It survives us being wrong.
Notes: If asked "how do you know your parameters are right" — point at the sweep. We do not need them to be exactly right for the conclusion to hold.

## Slide 7: It did nothing. Three times.
1
Corrected the measure
No effect. The bias applied equally to both roads, so it cancelled.
2
Made the two roads differ
Still almost nothing. Only blocked arrivals moved, barely.
3
Diagnosed it
Controllers agreed 85% of the time. Green was not scarce, so allocating it badly cost nothing.
4
Allocated green duration
It worked. Choosing which road is binary; how long is where a bad measure costs you.
Notes: This slide is deliberately about failure. The third attempt is the one to dwell on: we found our own fix had raised capacity so much that nothing was scarce. That diagnosis is the actual engineering.

## Slide 8: Scooter feeder meets bus arterial
Chart: People moved
| Static PCU (deployed today) | Efficiency only | People per second (ours)
People moved | 34772 | 41099 | 36683
Chart: Worst approach wait (ticks) — lower is better
| Static PCU (deployed today) | Efficiency only | People per second (ours)
Worst approach wait | 31.5 | 184.5 | 37.1
+1,911 ± 848 more people moved than what is deployed today — and no road left starving
Notes: Point at the red bar on the right. That is our own first attempt, and it is unusable: it leaves one road red for minutes. Showing it is the point.

## Slide 9: We found the flaw in our own fix
The problem
Optimising green-seconds-per-vehicle treats a two-wheeler road as cheap — and therefore low value. It scored badly on exactly the thing being maximised.
The feeder starved: 184 ticks of waiting. In an Indian city those riders are the least able to absorb it.
The fix
We were optimising a proxy. Road efficiency is a constraint, not the goal.
So we score each road by people moved per second of green, with an explicit fairness term on accumulated red time.
Worst-case waiting fell from 184 ticks to 37 — a five-fold cut — while still beating what is deployed today.
Notes: If you remember one slide, remember this one. A team that finds the equity problem in its own result, and says so before being asked, is a team worth trusting.

## Slide 10: Two standard metrics turned out to be gameable
Average queue rewards refusing traffic
A road held at red fills up and then turns arrivals away. Those vehicles never enter the network, so they never appear in the statistic.
A plain fixed clock "beat" our controller by blocking about 100 more vehicles per run while serving fewer.
Mean delay hides starvation
Our first RL controller posted the lowest mean queue in the benchmark — by learning to keep some approaches permanently red.
Its 95th-percentile delay was 66 ticks against a fixed clock’s 27. Every claim we make now carries p95 and worst-case beside the average.
Notes: These are findings about how the field evaluates itself, not just about our code. Both were caught by our own benchmark, which is the argument for building one properly.

## Slide 11: Built to be installed, not just benchmarked
Safety shield
Minimum green, starvation limits, a guaranteed maximum pedestrian wait. The optimiser proposes; the shield disposes.
Fails safe
Kill a detector, drop comms, fail a signal head — each routes to a documented fallback and the UI says which.
Explains itself
Every phase change is logged with the pressures behind it and the constraint that overrode the optimiser.
Speaks in city units
Idle fuel, CO₂ and rupees per year, with every assumption listed and challengeable.
Notes: Keep this brisk — 30 seconds. It is table stakes, not the headline.

## Slide 12: Every number in this deck re-runs on demand
python scripts/reproduce_results.py
Re-measures every documented claim and exits non-zero if one has stopped being true.
10/10
claims reproduced
119
automated tests
CI
fails on drift
It verifies the results that went against us, too
The claim that our correction changes nothing when both roads carry the same traffic must keep coming back with a confidence interval spanning zero. If a future change makes that pass for the wrong reason, the build goes red.
Notes: This is the slide that separates us from a demo. Offer to run it live if they want.

## Slide 13: What we are not claiming
Parameters are estimates, not measurements
Lateral widths and headways are centre estimates. Calibrating them needs stop-line video from a real junction, which we have not done.
It trades vehicles for people
About 1,800 fewer vehicles move while 1,900 more people do. Whether a city wants that is a policy decision, not a technical result.
It loses where traffic is uniform
With every road carrying the same mix it is measurably behind the conventional controller. It pays only when roads differ and green is scarce.
The engine is not a traffic simulator
Final performance claims must be regenerated in SUMO with a heterogeneous vehicle set.
Notes: Volunteering limitations before being asked changes how the rest of the deck is heard. It is also the honest position.

## Slide 14: Measure the right thing
Control theory imported from the West assumes lane discipline. We modelled lane-less traffic from physics, showed the standard method mis-allocates green by 21%, and fixed the equity problem that correction created.
Every figure re-runs with one command — including the ones that went against us.
Notes: Close on the one-sentence version. Then offer the live demo: the Mixed fleet tab runs the whole study in front of them, and the control condition is a checkbox.