## Slide 1: SmartTraffic
Adaptive signal control built for lane-less Indian traffic · Design of Smart Cities
Rishab CV 24BCE5296
Martin Wills 24BCE5255
Notes: [0:00-0:25] We built an adaptive traffic signal controller. The part that is new is that it is designed for traffic without lane discipline. Everything I show you re-runs from the repository with one command.

## Slide 2: Signal theory assumes lane discipline
What the textbooks assume
Vehicles queue single file. One crosses per lane per headway. A fixed factor converts a bus or a scooter into "car equivalents".
What an Indian junction does
Two-wheelers filter into lateral gaps and cross two or three abreast where one car fits. What limits the stop line is lateral space — not a factor calibrated for moving traffic.
Chennai: 132 hours lost per driver per year, 16 km/h at peak · TomTom 2025
Notes: [0:25-1:10] Every adaptive system in the world is built on the left-hand column. Indian traffic is the right-hand column. That gap is the whole project.

## Slide 3: The conventional factor is 56% too high
Chart: Car-equivalents per vehicle
| Two-wheeler | Auto | Car | Bus
Static PCU (used today) | 0.5 | 0.8 | 1 | 3
Implied by real discharge | 0.32 | 0.66 | 1 | 1.8
21.5%
of green wasted at Indian traffic mixes
Held green after the queue has already cleared. Those seconds are taken from the cross street.
Our model reproduces the textbook figure for cars exactly, so it departs from convention only where lane discipline does.
Notes: [1:10-2:00] We derived discharge from physical width and headway instead. The car column being identical matters — where the old assumption holds, we agree with it exactly. We are not just picking numbers that suit us.

## Slide 4: We found the flaw in our own fix
Correcting the measure was not enough
Optimising green-seconds-per-vehicle treats a scooter road as cheap, so it scored badly on the very thing being maximised.
It starved that road: 184 ticks of waiting — minutes — falling on the riders least able to absorb it.
So we changed what we optimise
Road efficiency is a constraint, not the goal. The controller now scores each road by people moved per second of green, with a fairness term on accumulated red time.
Worst-case waiting fell from 184 ticks to 37 — a five-fold cut.
Notes: [2:00-2:55] This is the slide to dwell on. We found the equity problem in our own result and fixed it, rather than reporting the bigger number and hoping nobody asked.

## Slide 5: Scooter feeder meets bus arterial
Chart: People moved
| Static PCU (deployed today) | Efficiency only | People per second (ours)
People moved | 34772 | 41099 | 36683
Chart: Worst approach wait (ticks) — lower is better
| Static PCU (deployed today) | Efficiency only | People per second (ours)
Worst approach wait | 31.5 | 184.5 | 37.1
+1,911 ± 848 more people moved than what is deployed today — and no road left starving
Notes: [2:55-3:50] Ten seeds, paired confidence intervals. The red bar is our own first attempt — we show it because it is the reason the final controller is shaped this way.

## Slide 6: Every number re-runs on demand
python scripts/reproduce_results.py
Re-measures every documented claim and exits non-zero if one has stopped being true.
10/10
claims reproduced
122
automated tests
15
controllers benchmarked
What we are not claiming
Discharge parameters are estimates, not measurements from a real junction. It moves more people but fewer vehicles, which is a policy choice. And where every road carries the same traffic it is measurably behind the conventional controller.
Notes: [3:50-4:40] Say the limitations out loud. Volunteering them before being asked is what makes the rest of the numbers believable.

## Slide 7: Measure the right thing
Control theory imported from the West assumes lane discipline. We modelled lane-less traffic from physics, showed the standard method mis-allocates green by 21%, and fixed the equity problem that correction created.
Rishab CV · 24BCE5296 Martin Wills · 24BCE5255
Notes: [4:40-5:00] Close on the one-sentence version, then offer the live demo: the Mixed fleet tab runs the whole study on screen, and the control condition is a checkbox.